Circuit Verification

---
Code Structure
- Circuit design is specified using the following predicates:
  - connected(A,B) : terminal A is connected to terminal B
  - in(I,G) : Ith input terminal of gate G
  - out(G) : Output terminal of gate G
  - type(A,B) : A is of type B

---
Code Structure
- Main code contains codes for gates:
  - AND
  - OR
  - NOT
  - XOR
- Other predicates used are
  - Equal
  - Vaild
  - member

---
Evaluation
- 5 Input (X1,X2,X3,X4,X5), 1 output(Y)
- Call signal(X1,X2,X3,X4,X5, 0) to generate all inputs for which output is '0'.
- Call signal(X1,X2,X3,X4,X5, 1) to generate all inputs for which output is '1'.

---
Majority Circuit Observations
- 5 bit Majority circuit is implemented.
- signal(X1,X2,X3,X4,X5,1) is called.
  - Produced 10 possible inputs (as expected).
- signal(X1,X2,X3,X4,X5,0) is called.
  - Produced 22 possible inputs (remaining inputs).

---
Palindrome Circuit Observation
- 5 bit Palindrome circuit is implemented.
- signal(X1,X2,X3,X4,X5,1) is called.
  - Produced 8 possible inputs (as expected).
- signal(X1,X2,X3,X4,X5,0) is called.
  - Produced 24 possible inputs (remaining inputs).